## Slide 1: Coring
12.1-1

## Slide 2: Coring for ODP
Notes: The Ocean Drilling Program probably does more coring than anyone. Since the wells that ODP drill are purely scientific, they core the entire well, and use very innovative coring equipment.

## Slide 3: Planning
ODP
Virtually everything is cored – continuously
What goes into the planning
  What type of coring tools will be used

## Slide 4: How it is physically accomplished
Coring assembly is run on the bottom of the drilling assembly.
Weight is applied to the core bit and the drillstring is rotated.
Doughnut is cut by the core bit
Core is swallowed by the core barrel.

## Slide 5: Tools
Core Bits
Core Barrels

## Slide 6: Advanced Piston Corer
Schematic of the APC before and after stroking out the inner core barrel to take a core. Pump pressure inside the drill string severs the shear pins and allows the inner core barrel to stroke out 9.5 m in 2–3 s with ~27,000 lb of force. Comparison of sediment core quality between rotary drilling and piston coring.

## Slide 7: Advanced Piston Corer
Notes: The advanced piston corer takes core samples in soft formations. The piston is pushed down through the coring bit and swallows the core sample.

## Slide 8: Advanced Piston Corer Temperature
Continuous temperature measurements are recorded with the APCT core shoe embedded in the sediment.

## Slide 9: Extended Core Barrel
Schematic of the XCB retractable cutting shoe in standard coring mode. The XCB shoe extends 6 to 14 in. ahead of the bit in very soft formations and retracts ~7 in. (inside the main bit) as weight on bit exceeds about 12,000 lb (collapses a coil spring).
Notes: In a little harder (but still soft) formations ODP may use their Extended Core Barrel.

## Slide 10: Extended Core Barrel
An 11 in. APC/XCB bit and soft formation XCB cutting shoe.

## Slide 11: Rotary Core Barrel
Schematic of the RCB coring system in coring mode with a bare seafloor spud-in. A center bit can be run on the inner core barrel to drill ahead without core recovery.

## Slide 12: RCB Roller Cone Bit

## Slide 13: Advanced Diamond Core Barrel
Figure 1. Schematic of the ADCB showing the bit, outer core barrel, and inner core barrel. The ADCB is an adaptation of a mining style "PQ" coring assembly.

## Slide 14: Pressure Core Sampler
Schematic of the PCS in the "coring ahead" mode (with the ball valve open to accept core) (left). After cutting the core (right), the wireline is picked up to release the ball, which redirects fluid to lift the core tube for "core retrieval" mode (with the core tube and core retracted inside the tool and the ball valve closed). Arrows indicate fluid flow.

## Slide 15: Bits for PCS
There are three bits available for rotary coring with the PCS tool: RBI auger bit (A), Christiansen standard bit (B), and RBI PDC bit (C).

## Slide 16: Tripping
ODP uses wireline retrieval tools to remove the core without retrieving the coring assembly

## Slide 17: Storage and transport
Most ODP cores are analyzed on the rig, then the cores are transported to land.
Cores are then available for additional study by ODP personnel or by other interested parties.

## Slide 18: Coring for Industry
How does this differ from Scientific Coring by ODP?
  Industry is looking for different information.
  Industry is very interested in the time it takes to core and the cost.
  Industry is only interested in select formations – where we suspect commercial quantities of oil and gas are located.

## Slide 19: How it is accomplished
Essentially the same as ODP
There are some differences in tools

## Slide 20: Planning
Coring is time consuming and expensive.
Industry only wants to retrieve cores from formations that is suspects contain commercial quantities of oil and gas.
Core only these formations.
We have to predict what depth to core before we drill.

## Slide 21: Tools – Baker Hughes
Core bits
Core barrels

## Slide 22: CoreDrill Evaluation Coring
Where core points are uncertain or when coring appears to add excessive rig time, our CoreDrill system combines high ROP, quick inner barrel changes and fewer drillstring trips to produce good quality core samples at low cost.

## Slide 23: Oriented Coring
Special orienting tools scribe a mark on the core so that formation dip and strike can be determined from the core.

## Slide 24: CoreGard Low Invasion Coring
A system of low invasion drilling fluids, anti-whirl core bits and extended pilot shoe features minimizes fluid filtrate invasion of the core.

## Slide 25: Gel Coring
The INTEQ Gel Coring system preserves core wettability characteristics and mechanical integrity to gain quality information from formation samples
Features:
A pre-loaded inner barrel containing a non-invasive encapsulating gel and
Downhole encapsulation of the core sample to isolate it from the drilling fluid

## Slide 27: Anti-Whirl Technology
In certain formations and well paths, bit whirl may cause core damage or undergauge cores. Our coring engineers can determine when to use anti-whirl bit technology to minimize these problems.

## Slide 28: Anti-Whirl Technology

## Slide 29: Wellsite Core Evaluation
Our Wellsite Core Evaluation service is conducted in transportable laboratory modules. We can furnish quick preliminary evaluation of core samples, and also cut and preserve core samples for detailed laboratory analysis.

## Slide 30: High Pressure/Fluid Retained Coring
In-situ data gathering services employ proprietary pressure containing core barrels that collect and preserve intact formation samples and their fluids.

## Slide 31: Tripping
Industry does not generally use continuous coring operations.
We core 60 – 90 foot sections then retrieve the entire assembly.
If additional coring is necessary, the assembly is tripped back into the wellbore and coring is continued.

## Slide 32: Sidewall Cores
What are sidewall cores?
How is it accomplished?

## Slide 33: Why sidewall cores
Much cheaper than conventional cores
Core after drilling through the formations and have run electric logs
You do not core in zones where core data is not needed.
You can selectively retrieve formation samples.

## Slide 34: What information is gathered
Porosity
Fluid content and saturation
Permeability, relative permeability
Chemical composition
Particle size distribution
Rock strength

## Slide 35: Relative Permeability

## Slide 36: Why do we need this information?

## Slide 37: Drilling fluid selection – non damaging
We need to know the chemical composition of the formations of interest so that we can design a non-damaging drilling fluid.

## Slide 38: Stimulation
We need chemical composition so that we can plan a successful treatment
  Acidizing
  Hydraulic fracturing

## Slide 39: Formation strength
We can plan the correct drilling fluid density
We can plan for wellbore stability issues
We can plan sand control techniques

## Slide 40: Why protect the cores
Altered permeability
Altered porosity
Altered fluid content and saturations